updated: 23-FEB-1999

	    Some comments on Matlab tools developed for use at ATF

================================================================================

GENERAL REMARKS
---------------

We have developed some Matlab function and "mex" files for use in modeling and
analyzing ATF data.  These functions all reside on the ATFAXP machine in:

 USER$DISK1:[MDW.MATLAB]

To gain access to these commands you can either add the following commands to
your LOGIN.COM file:

 $ architecture = f$getsyi("ARCH_NAME")
 $ if (architecture.eqs."Alpha")
 $ then
 $    @matlab:[etc]matlab_sylogin
 $    matlabpath :== 'matlabpath'",user$disk1:[mdw.matlab]"
 $ endif

or issue the following command once you're in Matlab (note: >> is the Matlab
prompt):

 >> p=path;path(p,'user$disk1:[mdw.matlab]');

Most of the Matlab functions described below have online help available ...
just give the Matlab help command for the function you're interested in.  For
instance, to get help for the comf2mat function type:

 >> help comf2mat

In addition to online help, most of the functions are extensively commented
with information that we thought might be useful ... browse through the files
in [MDW.MATLAB] if you have further questions.


MATLAB MODELING TOOLS
---------------------

o atf_regions.m

  This function simply lists the defined ATF COMFORT modeling regions by name
  and number.

o comf2mat.mexag

  This program reads an unformatted COMFORT Twiss file from [MDW.MODEL] for a
  specified model region and uploads the contents directly into Matlab arrays.
  The online help consists of:

   [NAME,ITYPE,S,ENERGY,TWISS]=comf2mat(region);
 
   This function reads an unformatted COMFORT Twiss file and returns the
   contents as Matlab arrays. The Twiss file must reside in
 
      USER$DISK1:[MDW.MODEL]
 
   and must have a name of the form
 
      MODLSECT_nn.TWSS
 
   where nn is any 2 digit integer between 01 and 99 (01-07 are reserved for
   ATF model regions).
 
   INPUTS:
 
      region = [scalar] ATF MODEL region (1-5 are pre-defined; 6-99 are free
               to define as you like)
 
                1 = Linac
                2 = BT
                3 = DR first turn (starting at exit of injection kicker)
                4 = BT follwed by DR first turn
                5 = DR stored beam (starting at the center of QF2R.1)
                6 = EXT (starting at entrance of extraction kicker)
                7 = Linac followed by BT
 
   OUTPUTS:
 
      NAME   = a string array of 8-character element names
      ITYPE  = an integer array of element types
 
                1 = Drift                (DRFT)                                 
                2 = Bend                 (SBND)                                 
                3 = Quadrupole           (QUAD)                                 
                4 = Sextupole            (SEXT)                                 
                5 = Linear acceleration  (ACCL)                                 
                6 = Horizontal corrector (HKIC)                                 
                7 = Vertical corrector   (VKIC)                                 
                8 = H/V corrector        (KICK)                                 
                9 = Horizontal BPM       (HMON)                                 
               10 = Vertical BPM         (VMON)                                 
               11 = H/V BPM              (MONI)                                 
               12 = Marker point         (MARK)                                 
 
      S      = a real array of element S-positions [m]
      ENERGY = a real array of element energies [GeV]
      TWISS  = an nx10 real array of element Twiss parameters, where the order
               is [psix,betax,alphax,etax,etapx,psiy,betay,alphay,etay,etapy]
               (psix, psiy, and eta' in radians; beta and eta in meters)

o get_new_model.m

  This function does it all ... gets magnet currents, makes COMFORT input
  files, runs COMFORT, and uploads the resultant Twiss parameters.  The online
  help consists of:

  [NAME,ITYPE,S,ENERGY,TWISS,ksad]=get_new_model(region,fn);
 
  Get the model (Twiss parameters, etc) for a specified ATF region.
 
  INPUTS:
 
     region = [scalar] ATF model region number
 
               1 = Linac
               2 = BT
               3 = DR first turn (starting at exit of injection kicker)
               4 = BT follwed by DR first turn
               5 = DR stored beam (starting at the center of QF2R.1)
               6 = EXT (starting at entrance of extraction kicker)
               7 = Linac followed by BT
 
     fn     = (OPTIONAL,[string]) if provided, a setdata file name
              (i.e. 'SET97MAR14_2049') or 'design'; if not provided,
              quadrupole currents will be taken from the database and
              used
 
  OUTPUTS:
 
     NAME   = a string array of 8-character element names
     ITYPE  = an integer array of element types
 
               1 = Drift                (DRFT)                                 
               2 = Bend                 (SBND)                                 
               3 = Quadrupole           (QUAD)                                 
               4 = Sextupole            (SEXT)                                 
               5 = Linear acceleration  (ACCL)                                 
               6 = Horizontal corrector (HKIC)                                 
               7 = Vertical corrector   (VKIC)                                 
               8 = H/V corrector        (KICK)                                 
               9 = Horizontal BPM       (HMON)                                 
              10 = Vertical BPM         (VMON)                                 
              11 = H/V BPM              (MONI)                                 
              12 = Marker point         (MARK)                                 
 
     S      = a real array of element S-positions [m]
     ENERGY = a real array of element energies [GeV]
     TWISS  = an nx10 real array of element Twiss parameters, where the order
              is [psix,betax,alphax,etax,etapx,psiy,betay,alphay,etay,etapy]
              (psix, psiy, and eta' in radians; beta and eta in meters)
     ksad   = the computed SAD K1 values for the quadrupoles [1/m] (positive
              means "QF") ... will not be returned if fn='design'

o get_bt_quads.m

  This function performs the magnet current to magnet strength conversion for
  BT quadrupoles and returns both SAD strengths (G'L/brho [1/m]) and COMFORT
  strengths (G'/brho [1/m^2]).  The comments in this function fully describe
  how the scaling is done and where to find the data needed to perform the
  scaling.  The online help consists of:

  [energy,k1,ksad]=get_bt_quads(I,energy);
 
  Get BT beam energy, BT quad COMFORT K1s, and BT quad SAD Ks.
  (NOTE: assumes fudge factors are zero)
 
  Both input arguments are optional ... you can provide no inputs,
  I only, or both I and energy.  If you provide no inputs, the quad
  currents and BT energy are taken from the database.  If you provide
  I only, the BT energy is taken from the database.
 
  If you provide I, the order of currents must be:
 
     QD10T,QF10T,QD11T,QF11T,QD12T,QF20T,QF21T,QD30T,QF30T,QD31T,QF31T,
     QD32T,QF40T,QD40T,QF41T,QD41T,QF42T,QD42T,QF43T,QD50T,QF50T,QD51T,
     QF51T,QF52T,QD52T,QF53T,QM8R,QM9R
 
  INPUTS:
 
     I      = BT quad currents (amps) [28 element array]
     energy = BT energy (GeV)         [scalar          ]
 
  OUTPUTS:
 
     energy = BT energy (GeV)
     k1     = BT quad COMFORT K1s (1/m^2; negative means "QF")
     ksad   = BT quad SAD K1s (1/m; positive means "QF")

o get_dr_quads.m

  This function performs the magnet current to magnet strength conversion for
  DR quadrupoles and returns both SAD strengths (G'L/brho [1/m]) and COMFORT
  strengths (G'/brho [1/m^2]).  The comments in this function fully describe
  how the scaling is done and where to find the data needed to perform the
  scaling, including fudge factors.  The online help consists of:

  [energy,k1,ksad]=get_dr_quads(I,energy);
 
  Get DR beam energy, DR quad COMFORT K1s, and DR quad SAD Ks.
 
  Both input arguments are optional ... you can provide no inputs,
  I only, or both I and energy.  If you provide no inputs, the quad
  currents and DR energy are taken from the database.  If you provide
  I only, the DR energy is taken from the database.
 
  If you provide I, the order of currents must be:
 
     QF2R,QF1R,QM1R,QM2R,QM3R,QM4R,QM5R,QM6R,QM7R,QM8R,QM9R,QM10R,
     QM11R,QM12R,QM13R,QM14R,QM15R,QM16R,QM17R,QM18R,QM19R,QM20R,
     QM21R,QM22R,QM23R
 
  INPUTS:
 
     I      = DR quad currents (amps) [25 element array]
     energy = DR energy (GeV)         [scalar          ]
 
  OUTPUTS:
 
     energy = DR energy (GeV)
     k1     = DR quad COMFORT K1s (1/m^2; negative means "QF")
     ksad   = DR quad SAD K1s (1/m; positive means "QF")

o read_setdata.m, read_setdata_file.mexag

  This function reads quadrupole magnet currents from a SETDATA file.  The
  online help consists of:

  I=read_setdata(region,fn);
 
  Read magnet current values for the specified region from the specified
  SETDATA file.
 
  INPUTS:
 
     region = [scalar] ATF model region number
 
               1 = Linac
               2 = BT
               3 = DR first turn (starting at exit of injection kicker)
               4 = BT follwed by DR first turn
               5 = DR stored beam (starting at the center of QF2R.1)
               6 = EXT (starting at entrance of extraction kicker)
               7 = Linac followed by BT
 
     fn     = [string]) a setdata file name (i.e. 'SET97MAR14_2049')
 
  OUTPUTS:
 
     I      = quadrupole currents for the specified region, sorted into the
              appropriate order for use with get_ln_quads, get_bt_quads,
              get_dr_quads, or get_ext_quads

o make_comfort_file.for

  This program reads COMFORT quadrupole strengths from a file created by
  get_new_model and writes them into a copy of a COMFORT reference file.  The
  input file used by make_comfort_file consists of the model region number
  followed by the COMFORT K1 values for the quads in that region.  Note that
  the ordering of the quad strengths is crucial here ... see get_ln_quads,
  get_bt_quads, get_dr_quads, or get_ext_quads for the required order of quads.

o find_name.m

  This function allows you to search for a specific element name in the NAME
  array returned by comf2mat.  For example:

  >> id=find_name('ZH10T',NAME(:,1:5))

  returns a pointer to data for ZH10T (if it exists) in the arrays returned by
  comf2mat.

  A few notes on element names in the COMFORT decks:

  - All bends, quadrupoles, and sextupoles are split in half ... if you use
    find_name to get pointers to 'QF1R' after a COMFORT run that includes the
    DR, you will get a list of 56 pointers, 2 for each of the 28 occurrances in
    the DR model.  The first pointer for each QF1R is for Twiss parameters at
    the center of the quad, and the second for Twiss parameters at the exit

  - In the COMFORT decks occurrances of a given magnet type are not
    distinguished by occurrance number (e.g. QF2R.11) ... you'll have to count
    through the list of QF2R names to find the n'th occurrance.  For example,
    to find the Twiss parameters at the center of QF2R #11 (QF2R.11) do this:

    >> id=find_name('QF2R',N(:,1:4));
    >> QF2R11_twiss=TWISS(id(2*11-1),:);

    Be aware that this method of counting in the DR doesn't work when you use
    the first turn model ... there, the first QF2R in the element list is
    QF2R.8, which is the first QF2R that the beam coming from the BT sees.

  - BPM names in the DR are of the form "BPMnnR" rather than "M.nn" (for
    example DR BPM "M.23" is called "BPM23R" in the COMFORT files.


MATLAB BPM DATA ANALYSIS TOOLS
------------------------------

o atf_bpm_slopes.m
  (NOTE: I'm not sure if this one still works ... MDW 23-FEB-1999)

  This function (actually it is a Matlab "script") is used to analyze
  steer/BPM response data which has been acquired and saved into an ASCII file
  by a control system program written by N. Okugi.  You will have to supply
  some information in response to prompts as atf_bpm_slopes runs:

  - the ATF modeling region number (see atf_regions)
  - the fully qualified file specification for the data file (for example
    ATF$OPTICS_MEASURE:ZV51T97MAR27_1044.DAT)
  - data cut ... just enter zero
  - scanned device type (steer magnet or energy)
  - if steer device, whether x (ZH or ZX) or y (ZV or ZY)
  - whether or not to fit BPM slopes (this is slow ... if you want to redo the
    analysis on the same data after fitting slopes once, you can say "no" to
    this and save some time) 
  - the number of the first and last BPMs for which slope fits will be
    performed (be careful here ... if your modeling region isn't #5 the BPM
    "numbers" won't be what you expect ... look carefully at the table of BPM
    numbers presented just before this prompt)
  - whether to fit R12s only or to fit both R11s and R12s

  If everything works, you'll end up with a plot of the fitted BPM slopes with
  error bars overlaid with the fitted values, as well as an estimate of the
  steering corrector strength (um/amp).

There are other data analysis tools in [MDW.MATLAB], as well as parts of
atf_bpm_slopes which can be run on their own.  Please browse through the files
in [MDW.MATLAB] and use whatever looks useful.