Draft data tables for CCR for on-surface detector assembly. 	August 29, 2006

Need to note that assumptions may be tentative and will be continued to be refined.

| Parameter | Vancouver BCD | After this CCR |
| --- | --- | --- |
| Number of collider halls | Two halls longitudinally separated by 138m | Single collider hall at z=0m |
| Size of single hall, W*L*H | 32*72*41.73m (125,765 CY was included into cost) | 30*100*35m (Note 0) |
| Shielding between halls | Natural due to separating soil/rock | Concrete shielding wall 3m thick, (1), (2) |
| Access shafts in collider hall | 15m shaft per hall, empty | Two 15m shafts, one in each end of the hall, equipped with elevator and stairs, which take out 3.6m wide segment of the shaft (3) |
| Detector service cavern | Yes, one cavern between two halls, 50*17*19m (4,682 CY was included in cost) (4) | None |
| Personnel access shafts in collider hall | 9m shaft in the detector service cavern, equipped with elevator and stairs | No additional shafts. Access via main 15m shafts |
| The need for concrete cover on top of the shafts | Not defined | Not needed for radiation protection. Partial cover is needed for on-surface assembly procedure |
| Building on surface for detector assembly | Large building was not needed, but the cost estimation included 21,692 sq ft building for each hall | Single surface building for detector assembly, size approximately 30*100m (32,291 sq ft) |
| Movable crane in surface building | 80t crane in each surface building | 400t single crane |
| Fixed gantry crane on surface | 1000t, rented for 1.5 years, installed above the 15m shafts | Two 2000t cranes, rented for 1.5 years each, installed above the 15m shafts (5) |
| Cranes in underground halls | Four cranes in total, 20t each | Two 400t cranes in each part of the collider hall (6) |
| The need for steel platforms in Detector hall, shape, number of storeys, lifts? | Was not defined | ? |
| Requirements for electrical supply |  | ? |
| Number and dimensions of largest penetrations (cables, pipes..) through shielding wall between service and detector halls or between two halves of the single hall? | Was not defined | ? |
| Survey driven requirements | Survey galleries were included | TBD |
| Any requirements in terms of safety that would have an impact on CFS? | ? | ? |

Notes:

0) The present estimation for GLD hall with on surface assembly calls for 56.5m length of the parts of the hall.

1) Default assumption is that shielding wall takes the full height of the hall, and separates the hall by two completely independent pars. Two independent cranes required in this case. It is also investigated if a partial wall could be acceptable (from radiation safety point of view), if it is aided by two curtain walls which travel on the rails of the crane. A single crane would be needed in this case. Detailed design of the wall will be done after CCR. The wall may not be needed if detectors are self shielded.

2) Attach radiation physics calculations showing that 3m wall is needed for not self-shielding detectors.

3) Attach scheme

4) Seems the sizes and volume do not match!

5) If schedule allows sequential installation of detectors, this would be single crane rented for longer period.

6) Cost of cranes >100t rise fast due to custom order. Detector assembly procedure still under discussion and the capacity of underground crane may reduce.